Pseudo code main

the iteration inside the while loop happens for every cycle
for every cycle the empty vector of vectors is initialised
a default channel 0 is initialised
default in the case of no need for parallel communications ?
for every node in the chip, a loop collects the nodes that wish to transmit
if the nodes’ buffer isn’t empty then a couple is created: [node_id, channel_id]
the channel is the default
for every protocol, is sent the vector of couples for all transmitting nodes & default channels
should every node have the same channel??

channel function

get the channel id associated to the node given
if the channel assigned is 0
assign a random number in the list of possibles
must be able to delete said channel from possibles ? Creation of a list ?
if not
ok and continue

MAC PROTOCOLS

brs

for every channel contained in the list of possible channels (given in the global parameters)
if the channel is idle
for every node in in the vector of couples
initialising a vector of Nodes which <ill be fed to the protocol buffer
if the channel assigned to the node is present in the list of possibles
the packet is cast to the protocol_type packet
if backoff = 0, then transmission
set the channel busy
push ids of nodes to concurrent_tx (id specific)
channel_function

if the channel is busy
for every node wanting to transmit
if nodes have same channel id
push ids to concurrent_tx (channel specific)
if node finished transmitting
delete
get list of concurrent_tx (channel specific)
the packet is cast to the protocol_type packet
if backoff = 0 transmission
channel_function
normally no more collisions here ???
set medium to idle
if only one node is transmitting
the packet is cast to the protocol_type packet
channel_function

token

for every channel contained in the list of possible channels (given in the global parameters)

while we are still transmitting
the packet is cast to the protocol_type packet
if the amount of packets haven't been able to be transmitted, increase the throughput
if there are no cycles lefts the transmission was successful
empty the vector of transmitting nodes, leaving only one as token holder
set the medium to idle
else, must find a solution for possible collisision??
channel_function
if the medium is idle
look for the token holder in the list of nodes that are ready to send (token holder=packet)
if found, token holder starts transmitting
the packet is cast to the protocol_type packet
if amount of packets haven't been transmitted, increase throughput
if there are no cycles lefts the transmission was successful
empty vector of transmitting nodes, leaving only one as token holder
set the medium to idle
else, must find a solution for possible collisision??
channel_function
if not found, the token is passed
update token current node